## Slide 1: Pulse width modulation generator
Student: Gherman Teodora Stefania
Group: 2023
Year: 2

## Slide 2: Table of contents
Introduction
PWM generator circuit
Block diagram
  Duty cycle control
  Amplitude control
Simulations
  Parametric sweep

## Slide 3: 1. Introduction

## Slide 4: What is pulse width modulation?
Pulse-width modulation (PWM) is a modulation process or technique used in most communication systems for encoding the amplitude of a signal right into a pulse width or duration of another signal, usually a carrier signal, for transmission.

## Slide 5: What is the duty cycle?
The term duty cycle describes the proportion of 'on' time to the regular interval or 'period' of time; a low duty cycle corresponds to low power, because the power is off for most of the time.

## Slide 6: 2. PWM generator circuit

## Slide 7: The circuit
Components:
1 (one) 555 timer chip
1 (one) operational amplifier
2 (two) capacitors
3 (three) potentiometers
6 (six) resistors
Desired values (ideal):
5kHz (200us period)
[60%; 80%] duty cycle
[2V, 8V] amplitude

## Slide 8: 3. Block diagram

## Slide 9: Block diagram
Astable multivibrator
Voltage regulator
(amplitude control)
RRC network -> Duty cycle control

## Slide 10: Duty cycle control
Parameter set10 is equal with:
0 80% duty cycle
1 60% duty cycle
Obtained values (real):
1.5% smaller period for 0.86% bigger duty cycle (60.52%)
5% smaller period for 0.38% smaller duty cycle (79.69%)

## Slide 11
60.52% duty cycle
79.69% duty cycle

## Slide 12: Amplitude control
Parameter set20 is equal with:
0 2V amplitude
1 8V amplitude
Obtained values (real):
with 0.5% smaller amplitude (7.96V)
with 0.55% higher amplitude (2.011V)

## Slide 13
2.011V amplitude
7.96V amplitude

## Slide 14: 4. Simulations
Parametric sweep

## Slide 15: Dependence of the duty cycle with POT11 and POT12
For:
0 79.96%
0.25 74.87%
0.5 70.10%
0.75 65.44%
1 60.52%

## Slide 16: Performance analysis

## Slide 17: Dependence of the amplitude with the POT21
For:
0 2.011V
0.25 3.48V
0.5 4.97V
0.75 6.46V
1 7.96V

## Slide 18: Performance analysis

## Slide 19: Thank you!